MITIGATION MEASURE ANALYSIS:  ALASKA PENINSULA

The following instructions are provided for guidance to adequately complete the Mitigation Measure Analysis form.

- The applicant shall respond to each Mitigation Measure, and all subsets of mitigation measures; i.e. A.2.d.i should be addressed and A.2.d.ii, and so forth.

- The applicant’s response shall begin by clearly indicating if the mitigation measure is satisfied, an exception is requested, or if the mitigation measure is not applicable.

- The applicants’ response shall then address how the proposed project clearly satisfies the mitigation measure, meets the intent of the mitigation measure, is not practicable, or is not applicable.

- The applicant shall verify working ‘in consultation with’ parties other than Department of Natural Resources (DNR), Division of Oil and Gas (DO&G) by reporting meeting dates and parties present for Mitigation Measures which require consultation with parties other than DNR, DO&G; i.e. Mitigation Measure 1.b.

Please note that this form, along with the Plan of Operations Application form and the Plan of Operations, must be adequately completed before DNR DO&G will review an application for potential approval.

| Alaska Peninsula | Company Response |
| --- | --- |
| A. Mitigation Measures |  |
| 1. Facilities and Operations |  |
| 1. A plan of operations must describe the lessee’s efforts to minimize impacts on residential, commercial, and recreational areas, Native allotments and subsistence use areas. At the time of application, lessee must submit a copy of the proposed plan of operations to all surface owners whose property will be entered. | A.1.1. |
| 2. Facilities must be designed and operated to minimize sight and sound impacts in areas of high residential, commercial, recreational, and subsistence use and important wildlife habitat. Methods may include providing natural buffers and screening to conceal facilities, sound insulation of facilities, or by using alternative means approved by the Director, in consultation with OHMP. | A.1.2. |
| 3. The siting of facilities, other than docks, roads, utility or pipeline corridors, or terminal facilities will be prohibited within one-half mile of the coast, barrier islands, reefs and lagoons, 500 feet of all fish bearing waterbodies and 1,500 feet from all current surface drinking water sources. Additionally, siting of such facilities will be prohibited within one-half mile of the banks of the Igushik, Naknek, Egegik, King Salmon (tributary to Egegik), David, Milky, Ugashik, King Salmon (tributary to Ugashik), Cinder, Meshik, Ilnik, Muddy, Sandy, Bear, Nelson, Caribou, Sapsuk and Dog Salmon Rivers, Black Hills, Steelhead, Painter and Pumice Creeks, Becharof and Ugashik Lakes and Franks Lagoon. Facilities may be sited within these buffers if the lessee demonstrates to the satisfaction of the Director, in consultation with OHMP and the affected local borough government, that site locations outside these buffers are not feasible and prudent or that a location inside the buffer is environmentally preferred. Road, utility, and pipeline crossings must be consolidated and aligned perpendicular or near perpendicular to watercourses. | A.1.3. |
| 4. The siting of temporary and permanent facilities will be prohibited within the Bristol Bay Fisheries Reserve. | A.1.4. |
| 5. Impacts to important wetlands must be minimized to the satisfaction of the Director, in consultation with OHMP and ADEC. The Director will consider whether facilities are sited in the least sensitive areas. Further, all activities within wetlands require permission from the US Army Corps of Engineers. | A.1.5. |
| 6. Pipelines must utilize existing transportation corridors and be buried where conditions permit. In areas with above ground placement, they must be designed, sited, and constructed to allow for the free movement of wildlife. Pipeline gravel pads must be designed to facilitate the containment and cleanup of spilled fluids. Pipelines must be designed and constructed to assure integrity against climatic conditions and geophysical hazards. | A.1.6. |
| 7. Drilling in offshore tracts will only be conducted directionally from onshore locations. | A.1.7. |
| 8. Pipelines that must cross marine waters will be constructed beneath the marine waters using directional drilling techniques, unless the Director, in consultation with OHMP and the local borough and CRSAs, approves an alternative method based on technical, environmental, and economic justification. | A.1.8. |
| 9. Dismantlement, Removal and Rehabilitation (DR&R): Upon abandonment of material sites, drilling sites, roads, buildings or other facilities, such facilities must be removed and the site rehabilitated to the satisfaction of the Director, unless the Director, in consultation with DMLW, OHMP, DEC, an affected local borough, and any non-state surface owner, determines that such removal and rehabilitation is not in the state’s interest. | A.1.9. |
| 10. Gravel mining within an active floodplain is prohibited. Gravel mining in upland sites will be restricted to the minimum area necessary to develop the field in an efficient manner. | A.1.10. |
| 2. Fish and Wildlife Habitat |  |
| 11. Detonation of explosives within or in proximity to fish bearing waters must not produce instantaneous pressure changes that exceed 2.7 pounds per square inch in the swim bladder of a fish. Detonation of explosives within or in close proximity to a fish spawning bed during the early stages of egg incubation must not produce a peak particle velocity greater than 0.5 inches per second. Blasting criteria have been developed by ADF&G and are available upon request. The location of known fish bearing waters within the project area can be obtained from the OHMP. | A.2.11. |
| 12. Compaction or removal of snow cover overlying fish bearing waterbodies is prohibited except for approved crossings. If ice thickness is not sufficient to facilitate a crossing, ice or snow bridges may be required. | A.2.12. |
| 13. Water intake pipes used to remove water from fish bearing waterbodies must be surrounded by a screened enclosure to prevent fish entrainment and impingement. Screen mesh size shall be no greater than 0.1 inches unless another size has been approved by OHMP. The maximum water velocity at the surface of the screen enclosure may be no greater than 0.2 feet per second. Screen material must be corrosion resistant, and must be adequately supported to prevent excessive sagging which could result in unusable intake surface. The intake structure must be designed and installed to avoid excessive fouling from floating debris, and a minimum of eight square feet of effective wetted screen surface must be provided for each multiple of a 450-gallon per minute (one cubic foot per second) pumping rate. The pump intake opening must be placed equidistant from all effective wetted screen surfaces. | A.2.13. |
| 14. Before commencement of any activities, lessees shall consult with ADF&G to identify the locations of known bear den sites that are occupied in the season of proposed activities. Exploration and development activities started between October 15 and April 30 may not be conducted within ½-mile of known occupied brown bear dens, unless alternative mitigation measures are approved by ADF&G. A lessee who encounters an occupied bear den not previously identified by ADF&G must report it to the Division of Wildlife Conservation, ADF&G, within 24 hours (King Salmon 907-2463340). Mobile activities shall avoid such discovered occupied dens by ½ -mile unless alternative mitigation measures are approved by the Director with concurrence from ADF&G. Non-mobile facilities will not be required to be relocated. | A.2.14. |
| 15. To minimize impacts to important waterfowl habitats in Kvichak Bay, Egegik Bay, Ugashik Bay, Cinder River Estuary, Port Heiden, Seal Islands Lagoon, Port Moller, Herendeen Bay, and Nelson Lagoon exploration, development, and major maintenance within these areas will only be allowed between November 16 and April 6, unless an exception is approved by the Director, in consultation with OHMP . Routine maintenance and emergency repairs will be permitted on a year-round basis during the production phase. A detailed plan describing routine maintenance activities to be conducted between April 7 and November 15 in these areas must be included in the plan of operations. | A.2.15. |
| 16. Cape Seniavin Walrus Haulout: Above ground lease-related facilities and structures will be prohibited within one mile inland from the coast, in an area extending one mile northeast and one mile southwest of the Cape Seniavin walrus haulout. | A.2.16. |

| 3. Subsistence, Commercial and Sport Harvest Activities |  |
| --- | --- |
| 17. Lease-related use will be restricted when the Director determines it is necessary to prevent conflicts with local subsistence, commercial and sport harvest activities. In enforcing this term DO&G, during review of plans of operation, will consult with other agencies, the affected local borough(s) and the public to identify and avoid potential conflicts. In order to avoid conflicts with subsistence, commercial and sport harvest activities, restrictions may include alternative site selection, requiring directional drilling, seasonal drilling restrictions, and other technologies deemed appropriate by the Director. | A.3.17. |
| 18. Traditional and customary access to subsistence areas shall be maintained unless reasonable alternative access is provided to subsistence users. “Reasonable access” is access using means generally available to subsistence users. | A.3.18. |
| 4. Fuel and Hazardous Substances |  |
| 19. Secondary containment shall be provided for the storage of fuel or hazardous substances. | A.4.19. |
| 20. Containers with an aggregate storage capacity of greater than 55 gallons which contain fuel or hazardous substances shall not be stored within 100 feet of a waterbody, or within 1,500 feet of a current surface drinking water source. | A.4.20. |
| 21. During equipment storage or maintenance, the site shall be protected from leaking or dripping fuel and hazardous substances by the placement of drip pans or other surface liners designed to catch and hold fluids under the equipment, or by creating an area for storage or maintenance using an impermeable liner or other suitable containment mechanism. | A.4.21. |
| 22. During fuel or hazardous substance transfer, secondary containment or a surface liner must be placed under all container or vehicle fuel tank inlet and outlet points, hose connections, and hose ends. Appropriate spill response equipment, sufficient to respond to a spill of up to five gallons, must be on hand during any transfer or handling of fuel or hazardous substances. Trained personnel shall attend transfer operations at all times. | A.4.22. |
| 23. Vehicle refueling shall not occur within the annual floodplain, except as addressed and approved in the plan of operations. This measure does not apply to water-borne vessels. | A.4.23. |
| 24. All independent fuel and hazardous substance containers shall be marked with the contents and the lessee’s or contractors name using paint or a permanent label. | A.4.24. |
| 25. A fresh water aquifer monitoring well, and quarterly water quality monitoring, is required down gradient of a permanent storage facility, unless alternative acceptable technology is approved by ADEC. | A.4.25. |
| 26. Waste from operations must be reduced, reused, or recycled to the maximum extent practicable. Garbage and domestic combustibles must be incinerated whenever possible or disposed of at an approved site in accordance with 18 AAC 60. | A.4.26. |
| 27. New solid waste disposal sites, other than for drilling waste, will not be approved or located on state property during the exploration phase of lease activities. Disposal sites may be provided for drilling waste if the facility complies with 18 AAC 60. | A.4.27. |
| 28. Drilling mud and cuttings cannot be discharged into lakes, streams, rivers, or important wetlands. On pad temporary cuttings storage will be allowed. Impermeable lining and diking, or equivalent measures, will be required for reserve pits. Injection of non-hazardous oilfield wastes is regulated by AOGCC through its Underground Injection Control (UIC) Program for oil and gas wells. See also Mitigation Measure 37f. | A.4.28. |
| 5. Access |  |
| 29. Exploration activities must utilize existing road systems, where practicable, or vehicles that do not cause significant damage to the ground surface or vegetation. Construction of temporary roads may be allowed. Construction of permanent roads may be allowed, upon approval by the Director in consultation with the local borough government. | A.5.29. |
| 30. Public access to, or use of, the lease area may not be restricted except within the immediate vicinity of drill sites, buildings, and other related facilities. Areas of restricted access must be identified in the plan of operations. Lease facilities and operations shall not be located so as to block access to or along navigable or public waters as defined in AS 38.05.965. | A.5.30. |
| 6. Prehistoric, Historic, and Archeological Sites |  |
| 31. Prior to the construction or placement of any structure, road, or facility resulting from exploration, development, or production activities, the lessee must conduct an inventory of prehistoric, historic, and archeological sites within the area affected by an activity. The inventory must include consideration of literature provided by nearby communities, Native organizations, and local residents; documentation of oral history regarding prehistoric and historic uses of such sites; evidence of consultation with the Alaska Heritage Resources Survey and the National Register of Historic Places; and site surveys. The inventory must also include a detailed analysis of the effects that might result from the activity. | A.6.31. |
| 32. The inventory of prehistoric, historic, and archeological sites must be submitted to the Director, and to SHPO who will coordinate with the local borough government for review and comment. If a prehistoric, historic, or archeological site or area could be adversely affected by a lease activity, the Director, after consultation with SHPO and the local borough, will direct the lessee as to the course of action to take to avoid or minimize adverse effects. | A.6.32. |
| 33. If a site, structure, or object of prehistoric, historic, or archaeological significance is discovered during lease operations, the lessee must report the discovery to the Director as soon as possible. The lessee must make reasonable efforts to preserve and protect the discovered site, structure, or object from damage until the Director, after consultation with the SHPO and the local borough, has directed the lessee as to the course of action to take for its preservation. | A.6.33. |
| 7. Local Hire, Communication, and Training |  |
| 34. To the extent they are available and qualified, lessees are encouraged to employ local and Alaska residents and contractors for work performed on the lease area. Lessees shall submit, as part of the plan of operations, a proposal detailing the means by which the lessee will comply with the measure. The proposal must include a description of the operator’s plans for partnering with local communities to recruit, hire and train local and Alaska residents and contractors. The lessee is encouraged, in formulating this proposal, to coordinate with employment and training services offered by the State of Alaska, the Southwest Vocational Education Training Center and local communities to train and recruit employees from local communities. | A.7.34. |
| 35. A plan of operations application must describe the lessee’s past and prospective efforts to communicate with local communities and interested local community groups. | A.7.35. |
| 36. A plan of operations application must include a training program for all personnel including contractors and subcontractors. The program must be designed to inform each person working on the project of environmental, social, and cultural concerns that relate to that person's job. The program must use methods to ensure that personnel understand and use techniques necessary to preserve geological, archeological, and biological resources. In addition, the program must be designed to help personnel increase their sensitivity and understanding of community values, customs, and lifestyles in areas where they will be operating. | A.7.36. |
| 8. Definitions |  |
| 37. In this document: a. "Facilities" means any structure, equipment, or improvement to the surface, whether temporary or permanent, including, but not limited to, roads, pads, pits, pipelines, power lines, generators, utilities, airstrips, wells, compressors, drill rigs, camps and buildings; b. "Feasible and prudent" means consistent with sound engineering practice and not causing environmental, social, or economic costs that outweigh the public benefit to be derived from compliance with the standard; c. "Important wetlands" means those wetlands that are of high value to fish, waterfowl, and shorebirds because of their unique characteristics or scarcity in the region or that have been determined to function at a high level using the hydrogeomorphic approach; d. "Minimize" means to reduce adverse impacts to the smallest amount, extent, duration, size, or degree reasonable in light of the environmental, social, or economic costs of further reduction; e. "Plan of operations" means a lease Plan of operations under 11 AAC 83.158 and a unit Plan of operations under 11 AAC 83.346; f. "Secondary containment" means an impermeable diked area or portable impermeable containment structure capable of containing 110 percent of the volume of the largest independent container plus 12 inches of freeboard. Double walled tanks do not qualify as Secondary Containment unless an exception is granted for a particular tank. g. “Temporary” means no more than 12 months. |  |